Dark solitons at nonlinear interfaces

J Sánchez-Curto1, P Chamorro-Posada1 and GS McDonald2

1 Departmento de Teor´ıa de la Se˜nal y Comunicaciones e Ingenier´ıa Telem´atica, Universidad de Valladolid, ETSI Telecomunicaci´on, Campus Miguel Delibes s/n, 47011 Valladolid, Spain

2 Joule Physics Laboratory, School of Computing, Science and Engineering, Materials & Physics Research Centre, University of Salford, Salford M5 4WT, UK

Abstract.

The refraction of dark solitons at a planar boundary separating two defocusing Kerr media is simulated and analyzed, for the first time (to our knowledge).  Analysis is based on the nonlinear Helmholtz equation and is thus valid for any angle of incidence.  A new law, governing refraction of black solitons, is combined with one describing bright soliton refraction to yield a generalized Snell’s law whose validity is verified numerically.  The complexity of gray soliton refraction is also analyzed, and illustrated by a change from external to internal refraction on varying the soliton contrast parameter.